## Slide 1: 5G Wizard
5G WIZARD

## Slide 2: New 5G Wizard
Automation
  Batching of multiple calculation
    Run any variation of inputs using multi-run calculations
    Total CDF calculation over single and multiple projects/designs
  Reporting
    HTML based reporting
    Results also written to JSON and HDF5 files for easy user access
Accuracy
  Implemented IEEE defined Power Density calculations (PD_N+, PD_Tot+,PD_Mod+)
  Rotating square averaging surface
  Validated using IEEE reference data
Speed
  100x faster than previous 5G Wizard
Open Source
  Built on pyAEDT library
  Supports Community Collaboration
  Customization to fit any workflow
  Publicly available on GitHub

## Slide 3: 5G Wizard Overview
Calculated maximum permissible exposure (MPE) and Cumulative Distribution Function (CDF) for 5G antenna modules
Radiation Characteristics Controlled by Codebook
  Magnitude and phase of antenna ports is defined through external “codebook” csv file
  Beam ID defines mag and phase on each port
MPE
  Power Density (PD, ie. W/m) evaluated on user defined surface
  Peak averaged PD (PD_N_+, PD_Tot_+, and PD_Mod_+)
CDF
  Statistical distribution calculated across beam ID’s
  Envelope antenna pattern and corresponding beam ID

## Slide 4
Cumulative Distribution Function

## Slide 5: 5G antenna array performance modeling
Antenna Beam Steering
  Antenna beam formed using look-up table: Code Book
  Look-up table imported into HFSS
    User can control beam by selecting corresponding beam ID
HFSS supports Code Book definition for port excitations
Beam pattern selected by Beam ID post processing variable
Beam ID | Port 1 | Port 2 | Port 3 | Port 4
1 | 1W @ 0° | 1W @ -145° | 1W @ -290° | 1W @ -435°
2 | 1W @ 0° | 1W @ -84° | 1W @ -168° | 1W @ -252°
3 | 1W @ 0° | 1W @ 0° | 1W @ 0° | 1W @ 0°
4 | 1W @ 0° | 1W @ 84° | 1W @ 168° | 1W @ 252°
5 | 1W @ 0° | 1W @ 145° | 1W @ 290° | 1W @ 435°
Automated
look-up table application to mm-wave array
using scripting
Beam Steering Code Book

## Slide 6: Evaluating spatial coverage capability for 5G mm-wave antennas
Example CDF: Probability of device to deliver 20.2dBm EIRP to 50% of observation points
Cumulative Distribution Function (CDF) for Antenna Arrays
  Statistical analysis of far field quantities that results in the probability that a quantity will be less than or equal to a certain percentage over the entire infinite far field sphere

## Slide 7: Evaluating CDF efficiently through simulation
3D Radiation Combined Pattern (Envelope)
Upper Hemisphere
2D Radiation Combined Pattern
View composite illumination capability over all steering angles
Provides insight into antenna system blind spots

## Slide 8: Evaluating human body effects on CDF
EIRP (dBm)
Isolated Device CDF Envelope Gain
Device+Body CDF Envelope Gain
Region of Human body
Shadow of Human body
Module 1
Module 2
Module 3
Device only: 3rd array adds 2.6 dB difference in 50th percentile CDF
Human body, 3 modules: Body degrades CDF by 1.3 dB
Phone with 3 mm-wave PAAs

## Slide 9
Power Density

## Slide 10: Maximum Permissible Exposure: Power Density
Automated extraction of Power Density enabled by HFSS
Efficient extraction for FCC certification process
  Featuring functions such as:
    Peak search and detection, area averaging, worst case beam pair phasing
5G Wizard: Automated PD Extraction

## Slide 11
Usage

## Slide 12: 5G Wizard: Setup
Project/Design
  Select from currently open projects and designs
Solution/Setup
  Select from currently solved solutions.
  Only solved points with saved fields will be selectable
Variation
  Selection from available solution variation
  Nominal is the variation that the design is currently set to
Note: Menu items will not refresh dynamically, exit wizard and reopen if something has changed in your desktop environments. For example, if you open a new project, complete a solution, or add a geometry, the menu items will not refresh until toolkit is reopened

## Slide 13: 5G Wizard: Codebook
Codebook
  CSV file that defines magnitude and phase of each port for a corresponding beam ID variable
Update Beam ID Codebook
  If a codebook has never been defined, this will import the codebook from a csv file and create 3 post processing variables
  These post processing variables will control the sources
    The codebook values will be imported into HFSS > Edit Sources, allowing the excitations to be controlled with beamID post processing variable
    For example, beamID can be set to any defined beamID and all ports will be updated
    UseBeamPair can be toggled between true and false to indicate that the beam pair should be also excited along with the primary beam

## Slide 14: 5G Wizard: Codebook Format
Codebook defined as CSV file
  Each row entry is separated by comma
  Multiple entries for a single column are separated by semi-colon “;”
Example provided and shown below
Organized as columns:
  BeamID
    Identification number (integer value)
  Module_Name (optional parameter)
    Useful for labeling output data
  Ant_Feed (Port Name)
    Port name as defined in your HFSS design
    Ports not listed are assumed to be not excited for that beam ID
    Amplitude and Phase correspond to location in adjacent columns
      Name_Port1;Name_Port2,Mag_Port1;Mag_Port2,Phase_Port1;Phase_Port2
  Amplitude
    Units in Watts if using Driven Modal and Volts if using Driven Terminal
  Phase
    Phase of corresponding port name in degrees
  Paired With
    Which beam ID to activate when beam pair is used
    Use “-1” if no beam pair exist
  Prad_Renorm (optional, Watts)
    Optional parameter allows renormalization of beam to user specified power
    If not included, power will not be renormalized and based on the values defined in the codebook or as user has defined in the GUI
      Using the codebook Prad_Renorm is useful in cases where you may be running multiple projects/designs/setups and each may have their own unique codebook
Optional

## Slide 15: 5G Wizard: Power Density
Evaluation Surface
  User defined, rectangular surface
  Can be model or non-model surface
  Can exist inside or outside of solved solution domain
PD Averaging Area
  Select from 1 or 4 cm^2, or create a user defined averaging area
  Area is used to used to calculate average PD using algorigthm defined in IEEE specification
  Sampling grid of fields is defined as 1mm or lambda/10, whichever is smaller
PD Type
  PD_N_+, PD_Tot_+ or PD_Mod_+
  Defined as equation (4), (5) and (8) in 63195-2
Power Renormalization
  Allows beams to be renormalized to a total radiated power
  A single value will renormalize all beams to that specified power
  Multiple values ie. 1,1.5,1,4 would renormalize each beam to the respective power.

## Slide 16: Cumulative Distribution Function
CDF Calculation:
  CDF relative to selected CS
  100th percentile renormalization can be applied to CDF output
CDF Report
Envelope Pattern: Shows maximum value when evaluated over all beam ID’s
Beam ID for Max: Shows which beam ID is used to achieve the maximum gain in every direction

## Slide 17: Multi-Run select
Allows multiple setup to be run sequentially
CDF Multi-Run Example File
PD Multi-Run Example File
Each row is considering a single job, where PD will be calculated for each job individually, and a summary across all jobs will also be reported. The columns correspond to the entries in the GUI
Each row is considering a single job, where CDF will be calculated for each job individually, and a summary across all jobs will also be reported. This allows one to calculate total CDF across multiple designs/projects

## Slide 18
Validation Data

## Slide 19: Validation Data
Poynting Vector
(Reference Data)
PD_N_+ (Local)
PD_N_+
(Averaged 1cm^2)
PD_N_+
(Averaged 4cm^2)
PD_Tot_+ (Local)
PD_Mod_+ (Local)
PD_Tot_+
(Averaged 1cm^2)
PD_Tot_+
(Averaged 4cm^2)
PD_Mod_+
(Averaged 1cm^2)
PD_Mod_+
(Averaged 4cm^2)
PD_N_+ (Local)
PD_N_+
(Averaged 1cm^2)
PD_N_+
(Averaged 4cm^2)
PD_Tot_+ (Local)
PD_Mod_+ (Local)
PD_Tot_+
(Averaged 1cm^2)
PD_Tot_+
(Averaged 4cm^2)
PD_Mod_+
(Averaged 1cm^2)
PD_Mod_+
(Averaged 4cm^2)
Reference Data
Provided by IEEE standard committee, based on original Poynting Vector reference data
5G Wizard Calculated from Poynting Vector reference data. The comparison show here will validate algorithms used in the 5G wizard for calculating local PD, and average PD
Comparison

## Slide 20: Local Comparison
PD_N_+ (Local)
PD_Tot_+ (Local)
PD_Mod_+ (Local)

## Slide 21: PD_N_+ Comparison: Averaging 1cm^2
PD_N_+
(Averaged 1cm^2)

## Slide 22: PD_N_+ Comparison: Averaging 4cm^2
PD_N_+
(Averaged 4cm^2)

## Slide 23: PD_Tot_+ Comparison: Averaging 1cm^2
PD_Tot_+
(Averaged 1cm^2)

## Slide 24: PD_Tot_+ Comparison: Averaging 4cm^2
PD_Tot_+
(Averaged 4cm^2)

## Slide 25: PD_Mod_+ Comparison: Averaging 1cm^2
PD_Mod_+
(Averaged 1cm^2)

## Slide 26: PD_Mod_+ Comparison: Averaging 4cm^2
PD_Mod_+
(Averaged 4cm^2)

## Slide 27: Comparison Summary
5G Wizard Calculation Time
  ~2.5 seconds for 1cm^2 surface per quantity
  ~ 3 seconds for 4cm^2 surface per quantity
Results are within 1% of reference data
Discussion:
The results will not be exactly the same because the reference data is based on analytic equations that can be re-evaluated at any requested point. In our simulations, and similar to how a measurement would be done, we are operating on a fixed grid of values that is not moved. For example, in the reference data, the grid of points to evaluate PD on is calculated. These points are fixed (x,y). When the average values are calculated at (x1,y1), a new set of grid points (x’,y’) are generated that align with the orientation of the averaging surface. As the averaging surface is rotated, a new set of points (x’,y’) are generated for each orientation.
No matter the orientation of the averaging square, a new set of points to evaluate that align with the averaging square. In the 5G wizard, because we are dealing with a fixed grid of points output from the simulation, when the averaging square rotates, for each rotation there may be a different set of points that fall within the averaging square. If a point does not fall within the averaging square at one rotation, it may fall within at another rotation.